## Slide 1: Aircraft fuel systems

## Slide 2: Fuel
Piston engines use octane fuel called aviation gasoline (avgas)
High grades of fuel can withstand high levels of compression without detonation with lead additives
Avgas colour codes:
Light aircraft = blue, 80 octane = red, 100 octane= green
Aircrafts can also operate on standard automotive gasoline called mogas
Mogas may contain alcohol additives to make it volatile and prone to fuel system vapour locks.
Fuel must be checked for contamination for example water
Water is denser then fuel and collects at points in the fuel system

## Slide 3: Fuel (part 2)
Gas turban engines use kerosene known as avtur
Kerosene is strew coloured and has a higher distillation cut
Avtur absorbs water more then avgas which tends to turn into ice/fuel gel
Engine heat is used to keep fuel ice-free
Some turbine power aircrafts fuel has supplied with anti icing additives
Specific gravity for gasoline is 0.7 and kerosene is 0.8

## Slide 4: Fuel storage and delivery ( light aircrafts)
Light aircraft can store from 20-100 gallons of fuel in tanks located under the wings
Baffles prevent fuel sloshing
Fuel pick up pipes are located away from under the fuel tanks to prevent impurities.
Fuel starvation or tank distortion in prevented by the fuel tank being vented to atmospheric pressure
an overflow drain prevents excessive pressure from building up by the heat of the sun.
High wing aircrafts use gravity to feed the fuel although electric fuel pumps ate needed for engine injection systems.

## Slide 5: Fuel storage and delivery (part 2)
Low wing aircrafts have the fuel located lower then the engines so fuel pumps are required to pump fuel into the carburettor
Before engine start electric fuel pumps are used to clear the fuel lines from vapour
Electric fuel pumps are left switched of during flight, in case any mechanical fuel pump fails to work.
A selector valve allows the polite to choose what fuel tank he wants to use.
Each engine is fitted with its own fuel gauge

## Slide 6: Fuel storage and delivery for commercial aircrafts.
A large aircraft can carry up to 45000 gallons of fuel

## Slide 7: Fuel delivery
A large 4 engine aircraft commercial aircraft uses 800 gallons per hour during cruise and 47 gallons per minute during take off

## Slide 8: Fuel jettison
When a aircraft takes off and suffers from a malfunction it will need to lose weight so it uses its jettison to reduce to weight
This is achieved though masts which are located at the rear of each wingtip
Fuel is stored : fuselage, wings, tail fin, horizontal stabiliser
Each of the tanks contain fuel pumps and the main tank contains jettison pumps
Pump inlets provide maximum usable fuel and avoid ingestion
Ram air scoops help to pressurise systems
Each tank is vented via vent surge tanks which return any fuel back to the main tanks.
Aircrafts are fuelled at a rate of 200 gallons per minute
The amount of fuel is measured very accurately and displayed on the flight deck.

## Slide 9: Fuel storage and delivery- military aircrafts
Because of the size smaller tanks are fitted into the aircraft to carry more fuel which leads to a complex structure
Military aircrafts carry extra fuel in drop tanks normally mounted under the wing and can be jettisoned and have self sealing valves which prevent fuel loss.

## Slide 10: In-flight refuelling
Many tankers have the capability of refuelling both by probe and drogue and boom receptacle
Probe and drogue method: a tanker trails a refuelling hose with a large drogue attached behind it and the receiving aircraft has to insert the probe. The tanker has one probe from the centre of the aircraft ad one from each of the wings.
Boom and receptacle method: in this one the tanker is responsible for inserting the boom into the receptacle.
Some helicopters can refuel either by a tanker aircraft or by a surface shape whilst still hovering.