## Slide 1: Aircraft environmental control systems

## Slide 2: Light aircraft cabin ventilation and heating
The aircraft requires heating and ventilation for windscreen demisting as well as passenger comfort
This is done my ducting fresh air through hot engine and exhaust manifold surfaces.
If an exhaust manifold leaks it can release poisonous carbon monoxide gases into the cabin so precautions are taken

## Slide 3: The need for an environmental control system for commercial and military aircrafts
Humans find it hard to breath at 15000 feet and an commercial aircraft cruises at 35000 feet
As you increase the altitude the temperature falls at a rate of 2 degrees per 1000 feet (6.5 degrees per 1000 meters)
When the sea level is 15 degrees the temperature outside the aircraft at 35000 feet is -54 degrees.
The air that is compressed by the engines is used to pressurise the cabin and supply hot or cold air
The electronics also need the temperature of the aircraft to be with in a reasonable level of -30 to +90 degrees

## Slide 4: Aircraft pressurisation
Aircraft pressurisation is done my a value which allows the flow of air out of the cabin to reach a required internal ambient pressure.
The aircraft cabin pressure is 8000 even at a altitude of 35000 feet.
For military aircrafts the crew has their own set of oxygen supplies
Military aircrafts are pressurised to 20000 feet.

## Slide 5: Aircraft cabin and cockpit heating
Heating is also needed to warm up an aircraft that has soaked down in freezing temperatures on the ground
Heating helps de-misting of windscreens, especially during descent and an cold altitude to a warm altitude.

## Slide 6: Aircraft cabin and cockpit cooling
The skin of the aircraft is heated because of the high speed and friction. The skin can be heated more than 100 degrees due to kinetic effect for subsonic commercial airlines.
The aircraft cockpit and cabin also receive heat through solar radiation
The electronic equipment inside the aircraft also give of heat as well as the people

## Slide 7: Aircraft cabin and cockpit ventilation
The air in the cabin is drawn, filtered, mixed with fresh air and re-circulated
In hot and humid climates moisture from the air can weight more then 30 grams per kg, if the cabin is cooled it would result in condensation and wet mist so the environmental control system removes the moisture from the air
The moisture levels decrease as the altitude increases

## Slide 8: Air conditioning
The main source of air for the air-conditioning units in air bled from the engine compressors
The compressed air is cooled as much as possible using ram air from outside
The air is then expanded across a turbine which drive a compressor drawing the ram air though a heat exchanger to reduce its energy further
The water is extracted and the cooled air is mixed with warm air to give a expectable temperature for the cabin heating or cooling.
Air-conditioning is required in the aircraft when the aircraft is switched of so auxiliary power units (APU) are used which can provide power for the electronic generators.
The aircraft can also be hooked to ground support carts for electrical and air supplies.

## Slide 9: Distribution systems
These comprise a complex system of ducts, sensors and valves
The air enters through overhead outlets
Air flows in a circular pattern and exit through the floor grilles
The exiting air goes below the cabin floor into the lower lobe from which 50% air is exhausted form the aircraft through an outflow valve
The air is replaced every 2-3 minutes
There are 20-30 air changes per hour