## Slide 1: Weapon systems

## Slide 2: Introduction
AAMS = air to air missiles
ASMS= air to surface missiles
ECM= electronic countermeasures

## Slide 3: Fighter weapons
AAM (air to air missiles) are the first choice because they have a much greater range then guns, and the aircraft does not need to be pointing to its target when the missile is fired.
The selection and lunch are controlled using aircraft management systems.
When a target is in rang the pilot will be notified on a heads up display or headset.
The pilot select the type of weapon using the weapon selecting switch.
The gyroscope in the missile navigate the missile and telling the missile what frequency the radar is
The missiles self tests all of its electronics
If the missile fails the self test then it wont launch (a hang-fire)
Guns (canons) have a shorter effective range.

## Slide 4: Ground/sea attack weapons
A ground attack aircraft can carry form 1 to 2 guns (cannons) of 20-30 mm calibre
They can fire at rates of 20-100 rounds per second
Because of heavy ammunition they only last up to 10 sec of firing
ASM (air to surface missiles) have very specialised weapons as they are designed to engage the target
Anti armour weapons have warheads which are designed to penetrate a very think armour plating
Anti radar weapons close in on sources of radar transmission for example surface to air missile sites, and destroy these sites by showering small fragments (shrapnel)
Anti ship weapons skim the surface of the sea to avoid being detected.
Missiles are able to “see” the target and identify the target by comparing the seeker image with the image programmed in the computer memory
A cruise missile is a very long range missile used in ASM ranged over 100km, they are programmed to fly using ground maps and terrain following

## Slide 5: Ground/sea attack weapons part 2
Cruise missiles are very accurate as the can strike within a few meter after travelling many kilometres.
Cruise missiles are lunched from aircrafts, ships or land vehicles
Ballistic means unguided weapons, and rockets are unguided weapons
Salvo is when many weapons are fired at ones
retarted bombs have small parachutes which slow down the bombs and allows the bomb to be dropped very accurately
Laser-guided bombs are a mixture of effectiveness and low cost. All that happens is they take a standard bomb and stick a laser detection systems and steerable fins
The target has a laser shined on it either by the aircraft of from a man on the ground and the missiles follows the laser energy reflected by the target
Laser bombs are very accurate this is known as “surgical bombing”- accurate bombing of targets with minimum damage to its surroundings
Cluster bombs open after being launched and release a number of bomb-lets this is highly effective against ground troops
Bomblets cover a rang of area and each bomblet has an armour piercing penetrator
The jp233 bomb contains a large number of smaller bombs which are used to scatter over a runway, they contain two types of Bomblets, one type creates deep creators in the runway and the other type is like a mine which explodes if lifted or tripped, causing great damage to vehicles and troops.

## Slide 6: Electronic/Defensive Systems
Below is measures to countermeasure missiles
The first is simple, it is to make it difficult to see the aircraft also known as “stealth”
The shape and size of the aircraft is also very important for stealth because of the amount of radar energy reflected.
A counter signal is used to met the incident signal to make it out as if the aircraft was somewhere else (false echoes)
Electrical noises are used to scramble or swamp the signal reflected. The systems mentioned above are electronic countermeasures.
Pyrotechnic flares are dropped to fool infra red missile systems, the flares are more intense then the infra red from the aircraft.
Clouds of chaff are strips of aluminium foil which reflect radar signals and this is a countermeasure against radar guided missiles.
It is also possible to destroy a missile with another missile called an anti missile missile

## Slide 7: How a missile system works
Locating and tracking the target:
The unit which detects and identifies the target is called the seeker
The seeker detects some forum of emission for example: radar emissions or reflection, infra-red emissions or reflection, optical sighting by an operator or magnetic influence
Most missiles work by detecting infra-red emissions or reflection or a radar
Radar seekers work of three forms : 1,active 2, semi-active or passive
An active seeker carries its own transmitter and detects reflections , this also gives the missile the ability to fire and forget capability which allows the aircraft that launches to depart straight away this seeker is mid ranged (15-30km maximum range)
Semi active seekers are used for greater range and for targets that are harder to locate, this seeker works in the same way as the active seeker but the lunch aircraft carries the transmitter which means the missile mass and power consumption is low, which means longer range and greater power. and the antenna can be larger because it is not limited by the size and power of the missile.
The disadvantages of this system is that the aircraft needs to keep the target illuminated which means staying within a danger area and giving your location away to the enemies
By using transmitted signals seekers can find out alto of information such as : targets position, range or time taken for reflected signal to return. With this information the missile can plot its rout.
A home on jam system is used if the target emits a jamming signal in an attempt to divert the missile, the missile enters a passive mode and uses the jamming signal itself to locate the target.

## Slide 8: How a missile system works part 2
Infra-red systems do not transmit but receive infra-red radiation
Flares are countermeasures against infra-red missiles, the flares dupe the missile to attack them rather then the aircraft
Missiles are becoming very sophisticated for exam imaging infra-red missile (I2R), this type compares the image of the target to the image programmed in the system and avoid any countermeasure. With this type of imaging you are able to pick the priority's. I2R are used in short rang weapons for example anti-ship, anti-aircraft and anti-armour. One disadvantage is that they are not made for long rang travel as they can only travel up to 15 or 20 km because infra-red signals are absorbed by the atmosphere
Multi mode missile use both radar and infra-red seeker systems.
Optical guidance are mostly used for ground launch missiles,

## Slide 9: Flight to the target
The lance rail: This is a small rail that holds the missile in place until it builds up its speed and lunches from the rail
Ejection lunch: this is when the missile is pushed away from the aircraft by gas operated rams at around 15-20 g
Ones the missile have lunched the rocket powered motor ignition takes place
Air to surface missiles are not lunched when the aircraft makes sever manoeuvres so the missile is released and the propulsion system is ignited before or after the missile is released.

## Slide 10: Motive power
For some missile solid fuelled rocket motors are used because they are reliable, easy and safe to handle and have a long maintenance free life. This motor is able to provide high thrust for a given volume and weight. Rocket motors are able to provide high thrust for a shot duration. Most of the flight time form the missile coasting (unpowered flight). For solid fuelled motors the thrust can not me controlled because the charge is mono-propellant which means it burns on its own supply of oxygen and will not stop until the oxygen burns out.
Gas turbine engine have longer thrust time because they do not need to carry a supply of oxygen so the missile has reduced fuel consumption which means longer thrust time (over 80km). Gas turbine rocket engines are useful for cruising missiles. The thrust of a gas turbine can be controlled by varying the fuel flow.
Ramjets can be used by a rocket motor to accurate to a high speed, this is sometimes done by putting the rocket propellant into the ram ducts, which takes over after the rocket motor burns out

## Slide 11: Control systems
Auto-pilot is used to steer the missile this is done by taking the target bearing and position information from the seeker and signals from the gyroscope and accelerometer to provide information of its target.

## Slide 12: Steering
Moving aerodynamic surfaces are used to steer the missile such would include:
fixed wings with moving tail fins
Fixed fin with moving wings
Fixed wings with moving canard
Or fins only
In short rang fights the missile can not make very high turn rates because of aerodynamic stalling so they might use the rocket nozzle to make the turns.
They use deflectors which are impinged into the motor to give thrust vector control or TVC
The disadvantage is that the deflectors suffer from rapid erosion so the missile is limited to short-range missiles.

## Slide 13: Power supply
Hydraulic power is used for: control surface actuators, gas supplies for pneumatic control-surface actuators, cooling of infra-red detectors.
Electrical power is generated by a thermal battery which gives high power for a short time. It has a very long shelf life. It generates power by exothermic (heat producing) chemical reaction
The electrical power produced is then passed through a stabilising circuit which splits the supply
Power is usually taken from the lunch aircraft through the umbilical cable
Hydraulic energy is stored in a hydraulic accumulator which is pressurised using nitrogen and initiated by firing a small pyrotechnic charge with burst the diaphragm and allows pressure to reach the oil
The advantages are long shelf like
Pneumatic energy may be stored under gas pressure or generated chemically
Cooling infra-red detectors requires a pure coolant gas such as nitrogen

## Slide 14: Destruction of the target
Safety and arming unit:
(SAU)- safety and arming unit
There is two types of fail-safety ( if something goes wrong the missile must stay in a safe condition)
The first is an electrical firing switch (EFS) this works by a timer, until the electrical firing switch is operated it prevents the firing signal to reach the explosive charge.
The second is a clockwork mechanism this works by the missiles forward acceleration to move part of the mechanism so that the warhead initiator charges align with holed in the casing called the shuttering
The missile must maintain a given acceleration for a minimum time for the (SAU) safety and arming unit to arm itself.

## Slide 15: Destruction of the target part 2
The fuze
The fuze detects when the missile hits the target or when it makes a close approach
The kill radius is the radius at which the missile can cause sufficient damage
When the missile is in optimum positing a firing signal will be sent to the (SAU) safety and arming unit which will initiate the warhead
There are two types of fuzes
The first called proximity fuze which detects the target from a distance and is radar or infra-red. They are insensitive to countermeasures such as flares for infra-red. The proximity fuze are used in anti-aircraft missile and cause damage from a distance.
The second called the contact fuze which only works if the missile hits the target. Anti-armour missiles use contact fuzes. Anti-ship weapons also use contact fuze but with a delay to the missile can penetrate deep inside the target.

## Slide 16: Destruction of the target part 3
The warhead:
Blast warheads use a very high pressure generated by the explosion to produce a blast wave.
Fragmentation and blast-fragmentation warheads contain pressure which it uses to break the warhead casing and propels fragments of shrapnel at high speed
The shape of the charge decided what the fragmentation pattern will be
Fragmentation warheads contain thousands of cubes (tungsten of 1 cm across) which on detonation are forced out at high speeds forming a cloud.
continuous-rod warheads are like the fragmentation warheads but contain steel bars which on detonation expand continuous ring which act like a circular saw.
Shaped-charge warheads are made to attack armour. The warhead is placed behind the seeker and the explosive is packed with a copper cone which forms a plasticised jet of copper which travels at a very high speed penetrating armour. Time must be allowed for this penetration so the detonation takes place before the missile reaches the target called stand off.
The attack reactive armour (explosives placed on the outside of the armour plate of the target) multiple shaped charges are used. The first charge sets of the reactive armour and the second charge attacks the armour which is then exposed.

## Slide 17: Location of parts
Seeker = placed at the nose
Control surface = position is dictated by aerodynamic constrains
Motor = at the aft (end) of the missile, motors account for 15-30% of the missile mass
Warhead= for anti-armour missile warhead is near the nose other wise it don't really mater
Seeker
fuze
psu
Electronics
warhead
Rocket motor
control